        SENSIRION COMPONENETS

1.HUMIDITY AND TEMPERATURE SENSOR

NAME	HUMIDITY RANGE (%)	TEMPERATURE RANGE(C)	HUMIDITY / ACCURACY / (%)	TEMPERATURE ACCURACY	VOLTAGE / REQUIRED / (V)
SHTW2	0-100	-30 - 100	+- 3.0	+- 0.3	1.62-1.98
SHTC3	0-100	-40 – 125	+-2	+-0.2	1.62-3.6
SHTC1	0-100	-30 -100	+-3	+-0.3	1.62-1.98
SHT35(SHT3X)	0-100	-40 - 125	+-1.5	+-0.1	2.15-5.5
SHT85	0-100	-40 – 105	+-1.5	+-0.1	2.15-5.5

NOTE-SHT85 is sensirion best in class component for humidity and temperature.
-It is long lasting in harsh conditions like dust and liquid.
-it is avilable in india at approx 1831 rs.
- It is compatible with arduino also.
-For use of SHTW2,SHTC3,SHTC1,SHT35 we required 1.sensor bridge for connecting sensors 2.run control software.
-SHT31 (design and development kit avilable ) having lcd display for humidity and temperature with blutooth low energy connectivity to ios or smartphones.

2.GAS SENSOR
PARAMETERS	SGP30	SGPC3	SVM30
OUTPUT	TVOC in ppb / H2 based CO2 in ppm	TVOC	TVOC in ppb / H2 based CO2 in ppm / relative humadity / temperature
SUPPLY VOLTAGE	1.62-1.98	1.62-1.98	4.5-5.5
AVG. CURRENT	48 mA	1mA	49mA
OUT. RANGE	TVOC:0-60000 ppb / CO2:0-60000 ppm	TVOC:0-60000 ppb	TVOC:0-60000 ppb / CO2:0-60000 ppm
TEMP. RANGE	-	-	-20 -85 (C) +-1(C)
HUM. RANGE	-	-	0-100 (%) +-5(%)

PM SENSOR(SPS30)

-Mass concentration accuracy = +-10µg/m3
-Particle size detection range = PM 1.0,PM 2.5,PM 4,PM 10
-operating temperature range= -10 to 60(C)
-supply voltage= -4.5 – 5.5(V)

       OTHER COMPANY SENSORS AVILABLE IN MARKET

1.TEMPERATURE AND HUMIDITY SENSOR(DHT22)

-It send data 2 second later according to serial monitor.
-supply voltage=3-5(V)
-Humidity range= +-2-5(%)
-temperature range= +-0.5(C)

2.GAS SENSOR

-MQ2 it can sense H2,LPG,CH4,CO,alcohol,smoke,propane.
-BME680 it can sense TVOC and CO2 with temperature and humidity but temperature and humidity accuracy is bad.
-CCS811 it having better accuracy then BME680 in sensing TVOC and CO2 .it cant give values of temperature and humidity.
-SGP30 can sense TVOC and CO2 but due to high sensitivity its accuracy is low.

3.PM SENSOR

3.1 HPM series
-long life more than 10 years.
-15% accuracy.
-current 80mA
-PM 1.0,PM 2.5,PM 4.0,PM 10.
-HPM115S0 (PM 2.5,PM 10)

3.2 PMS3003
-High -precision laser dust concentration sensor.
-range:PM(0.3-1.0),PM(1.0-2.5),PM(2.5-10)
-response time<=10sec.
-supply voltage=5V
-current=120mA
-temperature range=-20 - 50(C)